## Slide 1
Single-Channel ECG Sleep Stage Classification
Using 1D ResNet-34 on MESA Dataset
Supervisor:
Dr. Ibrahim Sadek
Eng. Merna Mansour
Eng. Veronicaa William
Five experimental variants · 5-class sleep staging
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 2
TEAM MEMBERS
  Baraa Tariq
  Eslam Mohamed
  Khaled Maayouf
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
BIO3609 – Biomedical Signal Processing Third Year – Biomedical Engineering Department Academic Year 2025-2026
GitHub: https://github.com/khaledmaaiof-bot/Sleep-Stages-Classification.git

## Slide 3
Why sleep staging matters
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
  Diagnose sleep apnea, insomnia, epilepsy, depression
  Gold standard = Polysomnography (PSG) → expensive, obtrusive, lab-based
Requires EEG, EOG, EMG, ECG, airflow, SpO₂
The research question
Can we classify sleep stages using only one ECG channel?
  Wearable-friendly (smartwatches, patches)
  Heart rate variability (HRV) reflects autonomic changes during sleep
  Enables at-home, longitudinal monitoring
Why ECG?
Based on MESA Sleep Study [1] and sleep medicine literature

## Slide 4
Challenge: N1 is physiologically subtle on ECG alone
Task Definition
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
5 sleep stages (30-second epochs)

## Slide 5
Dataset – MESA Sleep Study
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
Multi-Ethnic Study of Atherosclerosis (MESA)
  Overnight polysomnography with ECG + expert annotations
  Annotated in 30-second epochs by sleep specialists
Our extraction:
  Single ECG channel only (no EEG, EMG, EOG)
  Resampled to 256 Hz → 7,680 samples per window
  Bandpass filter: 0.5 – 40 Hz
Split: 80% train / 10% val / 10% test (stratified)

## Slide 6
Five Experimental Variants – Overview
We systematically compared five data balancing strategies:
All other components (model, split, loss) kept identical → fair comparison
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 7
Data Preprocessing Pipeline
Step-by-step (identical for all variants):
  Read EDF + XML annotation (pyEDFlib)
  Extract ECG channel (label contains 'ECG'/'EKG')
  Bandpass filter (0.5–40 Hz, zero-phase Butterworth)
  Resample to 256 Hz (uniform sampling)
  Parse XML sleep stages → map to 0–4 integer labels
  Slice 30-second windows (7,680 samples)
  Z-score normalize per window (mean=0, std=1)
Stratified split BEFORE any augmentation → prevents data leakage
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 8
Manual Augmentation (V3, V4, V6)
augment_ecg() – stochastic transformations:
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 9
Manual Augmentation (V3, V4, V6)
Balancing logic:
  Compute target = min_class_count × oversample_factor
  Minority classes → synthetic samples
  Majority classes → random downsampling
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 10
SMOTE (V7) – A Different Approach
SMOTE = Synthetic Minority Over-sampling Technique
  Generates samples by linear interpolation between real samples in feature space
  No signal-domain transforms
Our implementation:
  K-neighbors = 5
  Oversample factor = 10× min class
  Majority classes not downsampled
Key limitation:
  Linearly interpolated ECG windows may not be physiologically valid
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 11
Model Architecture – 1D ResNet-34
Adapted for time-series ECG (~21M parameters)
Residual connections enable deep training without degradation
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 12
Training Configuration (Shared)
Why class weights?
Natural class imbalance (N1 and N3 are rare) → penalizes errors on minority classes more strongly
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 13
Key Results – Test Performance
V6 achieved highest test accuracy (84.25%) and Kappa (0.7671)
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 14
Confusion Matrix V3
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
Confusion Matrix V6

## Slide 15
V3 Training curve
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
V6 Training curve

## Slide 16
Per Class Report V3
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering
Per Class Report V6

## Slide 17
Confusion Matrix Analysis (V6 Best Performer)
Key observations:
  Wake → excellent (92% correct, only 3% to N2)
  N2 → very good (85% correct)
  REM → good (83% correct)
  N3 → good (69% correct, 30% confused with N2)
Increasing the oversampling ratio from 6.4x (V4) to 10x (V3) significantly boosted the N1 classification accuracy from 23% to 37%.
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 18
Confusion Matrix Analysis (V6 Best Performer)
Common error patterns (physiologically expected):
- N1 ↔ N2 confusion (adjacent stages, subtle HRV differences)
- N3 ↔ N2 confusion (deep vs light slow-wave)
Best overall: V6 (84.25% Acc, Kappa=0.767)
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 19
Version Comparison – What We Learned
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 20
Val–Test Generalization Gap
V6 is the only version where test accuracy exceeded validation accuracy
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 21
Limitations & Challenges
  N1 is inherently ambiguous on ECG alone
  Cannot capture EEG-specific markers (spindles, K-complexes, delta waves)
Physiological limitations:
  SMOTE-generated ECGs not physiologically guaranteed
  Performance may degrade for arrhythmias not in MESA
Technical limitations:
  Not approved for clinical diagnosis (research only)
  Requires reliable R-peak detection (motion artifacts in wearables)
Clinical limitations:
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 22
Conclusions
Yes, a single-channel ECG can classify sleep stages
  Best model (V6): 84.25% test accuracy, Kappa = 0.7671
Manual ECG augmentation (noise, scaling, shift, wander) outperforms SMOTE
Larger batch size (32) improves gradient stability and generalization
Oversampling is critical – without it, model collapses (V5: 45.9%)
N1 remains challenging – future work needs better features or multimodal data
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 23
References
https://arxiv.org/abs/2412.01929
https://link.springer.com/article/10.1007/s40846-021-00646-8
https://www.semanticscholar.org/paper/5dac6c758ab1c2b0763e7cc4fb0ef28baa9c4c06
https://ieeexplore.ieee.org/document/10681551
[GitHub Repository Link]
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering

## Slide 24
THANK YOU
HELWAN UNI.
Faculty of Engineering
Department of Biomedical Engineering